## Slide 1: Intro to Hacking with the Raspberry Pi
Sarah Withee
@geekygirlsarah

## Slide 2: Hello!
I am Sarah Withee
Friendly polyglot software engineer
Hardware tinkerer
Robot builder
You can find me at @geekygirlsarah

## Slide 3: A Few Questions To Start…
Who has heard of the Raspberry Pi?
Who owns at least one?
Is it sitting in a closet/junk drawer?
Are you daunted at the idea of tinkering with hardware or electronics?
This talk is probably for you!

## Slide 4: A Few Questions To Start…
If you:
understand circuitry basics,
are familiar with breadboards and wiring,
and know how to program GPIO pins on the Pi
This talk may not be for you.
(I won’t be offended if you leave)

## Slide 5: Breakdown
Raspberry Pi Information and Models
Intro to Hardware
Intro to Programming Hardware
Project 1 - LEDs
Project 2 - Sensors
Project 3 – Push Buttons and LCD screen
Future Project Inspriation
Conclusion

## Slide 6
“The Raspberry Pi is a credit-card sized computer that plugs into your TV and a keyboard. It is a capable little computer which can be used in electronics projects, and for many of the things that your desktop PC does, like spreadsheets, word-processing and games. It also plays high-definition video. We want to see it being used by kids all over the world to learn programming.”
Raspberry Pi Foundation, raspberrypi.org/faqs

## Slide 7
“We are taking back the term ‘Hacking’ which has been soured in the public mind. Hacking is an art form that uses something in a way in which it was not originally intended. This highly creative activity can be highly technical, simply clever, or both. Hackers bask in the glory of building it instead of buying it, repairing it rather than trashing it, and raiding their junk bins for new projects every time they can steal a few moments away.”
Hackaday, hackaday.com/about/

## Slide 8: Resources
Slides, diagrams,
videos, and more!
sarahwithee.com/raspberrypi
very code
much resources
how to pi
total wow

## Slide 9: 1. Raspberry Pi Information and Models
The basics of this delicious computer

## Slide 10: History of the Raspberry Pi
2006 – Had idea for affordable computer for kids
2008 – Processors became cheap enough to make it feasible to build
2011 – 50 alpha boards, 25 beta boards, 10,000 production boards
2012 – Sold first units
2013 – Sold > 2M units
2015 – Pi 2 Model B and Pi Zero released
2016 – Pi 3 Model b released
2017 – Pi Zero W released

## Slide 11: Raspberry Pi Models
Pi Model A+
Pi 3 Model B+
Pi Model B+
Pi Zero
Pi 2 Model B
Pi Zero W

## Slide 12: Raspberry Pi Model Comparisons
 |  | Processor | Speed | Memory (shared w/GPU) | Expansion | USB Ports | Ethernet/ Wireless/ Bluetooth | Cost | Power Supply Needed
Pi Model A+ +* |  | ARMv6 (32-bit) | 700 MHz | 512 MB | Micro SDHC | 1 | None | $20 | 700 mA
Pi Model B+ * |  | ARMv6 (32-bit) | 700 MHz | 512 MB | Micro SDHC | 4 | 10/100 mbps | $25 | 1.8 A
Pi 2 Model B |  | ARMv8 (64-bit) | 900 MHz | 1 GB | Micro SDHC | 4 | 10/100 mbps | $35 | 1.8 A
Pi 3 Model B+ |  | ARMv8 (64-bit) | 1.4 GHz | 1 GB | Micro SDHC/ USB Boot | 4 | 10/100/1000, 802.11ac, BT 4.2 | $35 | 2.5 A
Pi Zero |  | ARMv6 (32-bit) | 1.0 GHz | 512 MB | Micro SDHC | 1 | None | $5 | 1.2 A
Pi Zero W |  | ARMv6 (32-bit) | 1.0 GHz | 512 MB | Micro SDHC | 1 | 801.11n, BT 4.1 | $10 | 1.2 A

## Slide 13: 2. Intro to Hardware
Wires and circuits and breadboards, oh my!

## Slide 14: Circuits
A complete route that electricity can travel through
🔌

## Slide 15: Intro to Hardware – Circuits
Series Circuit
Electricty can flow one direction
Close the switch to make the complete path
Open the switch to stop the electric flow

## Slide 16: Intro to Hardware – Circuits
Parallel Circuit
Electricty can flow more than one direction
Close the switch to make both paths complete
Open the switch to stop all the flow

## Slide 17: Breadboards
Device to quickly prototype circuits without solder

## Slide 18: Intro to Hardware - Breadboards
A literal breadboard
(http://www.instructables.com/id/Use-a-real-Bread-Board-for-prototyping-your-circui/)

## Slide 19: Intro to Hardware - Breadboards
Prototype Circuit
(https://learn.sparkfun.com/tutorials/how-to-use-a-breadboard)

## Slide 20: Intro to Hardware - Breadboards
Breadboard features
(https://learn.sparkfun.com/tutorials/how-to-use-a-breadboard)

## Slide 21: Intro to Hardware - Breadboards
Terminal Strips and Power Rails
(https://learn.sparkfun.com/tutorials/how-to-use-a-breadboard)

## Slide 22: Intro to Hardware – Breadboards
Circuits on Breadboards
Provide power to the power rails
Red – positive
Black/blue – negative
Use wires to connect components together

## Slide 23: Intro to Hardware – Breadboards
Circuits with Raspberry Pis
Use pin labelled “+3.3V” (volts) for postive
Use pin labelled “Ground” (GND) for negative

## Slide 24: Intro to Hardware – Breadboards
Circuits with Raspberry Pis
Note: Arduinos use 5V, be careful not to confuse the two

## Slide 25: GPIO
General Purpose Input/Output
Or how our projects “talk” to the Pi

## Slide 26: Intro to Hardware – GPIO
Raspberry Pi Pins
40 hardware pins
2 +3.3V
2 +5V
8 Ground
20 GPIO
2 Miscellaneous
Unfortunately, not labelled ON the Pi

## Slide 27: Intro to Hardware – GPIO
Raspberry Pi Pins
Of course, they’re not in any distinguishable order
(Pin diagram available at talk website)

## Slide 28: 3. Intro to Programming Hardware
The part you’re really here for

## Slide 29: Intro to Programming Hardware
On the Raspberry Pi, Python is built-in with GPIO libraries installed
Other languages available too

## Slide 30: Intro to Programming Hardware – Setup Commands
Pin Mode
First, pick your mode
Board – physical pin #
BCM – GPIO pin #

## Slide 31: Intro to Programming Hardware – Setup Commands
Next, import the GPIO library:
import Rpi.GPIO as GPIO
Then, set the mode (pick one):
GPIO.setmode(GPIO.BOARD)
GPIO.setmode(GPIO.BCM)

## Slide 32: Intro to Programming Hardware – Setup Commands
Pins used should be set to be input or output:
GPIO.setup(3, GPIO.OUT)
GPIO.setup(4, GPIO.IN)
You can change these later, not but setting them at all causes problems

## Slide 33: Intro to Programming Hardware – Output Commands
To write out to the output pins:
(pin number, value)
GPIO.output(3, True)
GPIO.output(10, False)
GPIO.output(6, GPIO.HIGH)
GPIO.output(22, GPIO.LOW)
True and HIGH are “on” (3.3 V)
False and LOW are “off” (0 V)

## Slide 34: Intro to Programming Hardware – Input Commands
To read from the input pins:
(pin number)
x = GPIO.input(4)
sensor.setValue(GPIO.input(15))
Values will be True/False or 1/0
(Note: Arudinos have analog value inputs. Raspberry Pis to not.)

## Slide 35: Intro to Programming Hardware – Cleanup Commands
Finally, when your program ends, you should “clean up” the pins:
GPIO.cleanup()
This stops reading inputs and stops sending outputs.

## Slide 36: Intro to Programming Hardware
Setup recap:
Import Rpi.GPIO library
Set pin mode (GPIO.BOARD or GPIO.BCM)
Set up input/output pins
Runtime recap:
Output a value to a pin number
Save input value from a pin to a variable

## Slide 37: 4. Project 1 - LEDs
The “Hello World” of electronics

## Slide 38: Project 1 - LEDs
8 LEDs that blink back and forth
Battlestar Galactica cylon
Knight Rider KITT car

## Slide 39: Project 1 - LEDs

## Slide 40: Project 1 - LEDs
Materials:
Raspberry Pi and power supply
1 breadboard
8 LEDs
8 resistors
9 jumper wires

## Slide 41: Jumper Wires
Pre-cut wires for prototyping with breadboards

## Slide 42: LED
Light-emiting diode
Like a small light bulb

## Slide 43: Project 1 - LEDs
LEDs
Diode – ensures electricity only goes one direction
(Wired wrong, it doesn’t work)
Anode – longer wire (+)
Cathode – shorter wire (-)
ALWAYS use a resistor

## Slide 44: Resistor
Slows down (or resists) the flow of electricity

## Slide 45: Project 1 - LEDs
Resistors
Can wire either direction
Band colors tell resistance value (in Ohms)
Without these, LEDs glow bright white, then element explodes

## Slide 46: Project 1 - LEDs
Wiring
Wire Pi’s ground to ground rail (black wire)
Plug in LEDs across gap

## Slide 47: Project 1 - LEDs
Wiring
Connect resistors from LED cathodes (-) to ground
Connect anodes (+) to Pi GPIO pins
GPIO pins become power sources

## Slide 48: Project 1 - LEDs
Programmatically turn on power to blue wires
Through LED & Resistor
Return to Ground
Through blue GND rail

## Slide 49: Project 1 - LEDs
# Import libraries
import RPi.GPIO as GPIO
import time
# Create array of GPIO pins
pins = [3, 5, 7, 29, 31, 26, 24, 21]
# Speed lights will blink (secs)
speed = .2 # Cylon-approved speed

## Slide 50: Project 1 - LEDs
# Set GPIO pins to board (physical pins) mode
GPIO.setmode(GPIO.BOARD)
# Set up all pins as output pins
for pin in pins:
GPIO.setup(pin, GPIO.OUT)

## Slide 51: Project 1 - LEDs
while True:
for i in range(len(pins)):
GPIO.output(pins[i], True)
time.sleep(speed)
GPIO.output(pins[i], False)
for i in range(len(pins)-1, -1, -1):
GPIO.output(pins[i], True)
time.sleep(speed)
GPIO.output(pins[i], False)

## Slide 52: Project 1 - LEDs
while True:
for i in range(len(pins)-1):
GPIO.output(pins[i], True)
time.sleep(speed)
GPIO.output(pins[i], False)
for i in range(len(pins)-1, 0, -1):
GPIO.output(pins[i], True)
time.sleep(speed)
GPIO.output(pins[i], False)

## Slide 53: Project 1 - LEDs

## Slide 54: 5. Project 2 – Sensors
Teaching computers to see.
Or something.

## Slide 55: Ultrasonic Distance Sensor
Looks like robot, but measures distance with timed sound waves

## Slide 56: Project 2 - Sensors
Ultrasonic Distance Sensor
Sends ultrasonic (high-pitched 40KHz) sound wave
Detects time it takes for sound to bounce back
Time tells it the distance

## Slide 57: Project 2 - Sensors
Ultrasonic Distance Sensor
4 pins:
VCC (power)
Trig (trigger)
Echo
GND (ground)
One side transmits, one receives

## Slide 58: Project 2 - Sensors
Ultrasonic Distance Sensor
Note: this works on 5V!
Don’t mix 3.3V and 5V together! (5V is bad for GPIO pins)
Use 1K resistor on Echo pin

## Slide 59: Project 2 - Sensors

## Slide 60: Project 2 - Sensors
Materials:
Raspberry Pi and power supply
1 breadboard
1 ultrasonic sensor (HC-SR04)
6 LEDs
6 resistors for LEDs
1 1K resistor
Jumper wires

## Slide 61: Project 2 - Sensors
Wiring
Wire Pi’s ground to ground rail (black)
Wire Pi’s +5V to power rail (red)
Wire both ground rails together (black wire)

## Slide 62: Project 2 - Sensors
Wiring
Wire LEDs and resistors to GPIO pins like in Project 1
Wire Trigger pin to GPIO

## Slide 63: Project 2 - Sensors
Wiring
Wire Echo pin to 1K resistor
Wire 1K resistor to GPIO

## Slide 64: Project 2 - Sensors
import time
import RPi.GPIO as GPIO
# Set up the pins
uTrig = 19
uEcho = 21
leds = [3, 5, 7, 11, 13, 15]
GPIO.setup(GPIO.BOARD)
for i in leds:
GPIO.setup(i, GPIO.OUT)
GPIO.output(i, GPIO.LOW) # off

## Slide 65: Project 2 - Sensors
def readDistance(trigger, echo):
GPIO.setwarnings(False)
GPIO.setmode(GPIO.BOARD)
GPIO.setup(trigger, GPIO.OUT)
GPIO.setup(echo ,GPIO.IN)
GPIO.output(trigger, GPIO.LOW)
time.sleep(0.3)

## Slide 66: Project 2 - Sensors
GPIO.output(trigger, True)
time.sleep(0.00001)
GPIO.output(trigger, False)
signaloff = 0
while GPIO.input(echo) == 0:
signaloff = time.time()

## Slide 67: Project 2 - Sensors
signalon = 0
while GPIO.input(echo) == 1:
signalon = time.time()
timepassed = signalon - signaloff
distance = timepassed * 17000
return distance

## Slide 68: Project 2 - Sensors
# Main program
while True:
# Grab a reading
read = readDistance (uTrig, uEcho)
for i in range(0, 6):
print(i)
if read > i * 3: # Every 3 cm
GPIO.output(leds[i], GPIO.HIGH)
else:
GPIO.output(leds[i], GPIO.LOW)

## Slide 69: Project 2 - Sensors

## Slide 70: 6. Project 3 – Push Buttons and LCD screens
Push it, push it real good

## Slide 71: Push Button
It’s a button you push

## Slide 72: Project 3 – Push Buttons and LCD screens
Push Button
Connects two pins when pressed
Fits across the breadboard gap

## Slide 73: Project 3 – Push Buttons and LCD screens
These two are connected
These two are connected
Pressing button connects all 4

## Slide 74: Project 3 – Push Buttons and LCD screens
Push Button
The curved pins should “hug” the breadboard gap

## Slide 75: LCD Screen
Screen that can display ASCII characters

## Slide 76: Project 3 – Push Buttons and LCD screens
LCD Screen
In a variety of row/col configurations
In a variety of pin configurations, but I recommend the I2C type

## Slide 77: I2C
Inter-Integrated Circuit, or “I squared C”
Communication protocol for electronics

## Slide 78: Project 3 – Push Buttons and LCD screens
I2C on the Raspberry Pi
It’s not enabled by default
Run sudo raspi-config
Go to Interfacing Options
Then I2C
Then enable
Then reboot

## Slide 79: Project 3 – Push Buttons and LCD screens
Wiring the LCD Screen
The 4 wires correspond to the 4 pins on the Pi:
Vcc – +5V
Gnd – Ground
SDA – SDA
SCL – SCL
(Yes, this you hook up to 5V)

## Slide 80: Project 3 – Push Buttons and LCD screens

## Slide 81: Project 3 – Push Buttons and LCD screens
Materials:
Raspberry Pi and power supply
1 breadboard
3 push buttons
3 LEDs and resistors
1 LCD screen
Jumper wires

## Slide 82: Project 3 – Push Buttons and LCD screens
Wiring
Connect ground to black rail
Connect LEDs like in project 1 (GPIO->LED->resistor->ground) (purple wires)

## Slide 83: Project 3 – Push Buttons and LCD screens
Wiring
Connect one side of each button to Ground (black wires)
Connect other side to GPIOs (cyan wires)

## Slide 84: Project 3 – Push Buttons and LCD screens
Wiring
Connect LCD’s Ground to Ground
Connect LCD’s Vcc to +5V on pi
Connect SDA/SCL to Pi pins 3/5 (orange wires)

## Slide 85: Project 3 – Push Buttons and LCD screens
(Open code in editor)

## Slide 86: Project 3 – Push Buttons and LCD screens

## Slide 87: 7. Future Project Inspiration
Time to flap those electronic wings and fly!

## Slide 88: Future Project Inspiration
Assorted ideas I’ve heard of:
Customized cookie maker machine
Show tweets/emails on LCD screen
AI-programmed remote control cars
Robots… of any variety…
Home automation (control heater/AC, control lights when in room, etc.)

## Slide 89: Future Project Inspiration
Pi Bluetooth Low Energy Cat Door
https://blog.adafruit.com/2017/09/15/rpi-3-ble-cat-door-raspberry_pi-piday-raspberrypi/

## Slide 90: Future Project Inspiration
Christmas Light Controller System
https://chivalrytimberz.wordpress.com/2012/12/03/pi-lights/

## Slide 91: Future Project Inspiration
Pi-Powered CNC Oreo customizing machine
https://blog.adafruit.com/2014/03/14/peek-inside-a-pi-powered-cnc-oreo-customizing-machine-raspberry_pi-piday-raspberrypi/, start at 3:40

## Slide 92: Future Project Inspiration
Where can I buy parts?
Pi: MicroCenter, Element14, Adafruit, Pishop.us. (Beware, Amazon costs > $35)
Power supply: MicroCenter, Amazon, $10-20
Breadboard: Amazon, MicroCenter, $4-7
Jumpers: Amazon, $3-7 for setsLEDs: Buy as kit (LEDs + resistors) on Amazon or electronic stores
Sensors: Amazon has kits for $15-40 (like https://www.amazon.com/OSOYOO-Modules-Mega2560-Raspberry-Learning/dp/B00WQY2704/)

## Slide 93: Future Project Inspiration
Final thoughts:
Development projects always take longer than you think. More so with hardware.
Hardware sometimes fails randomly. If software quits working, try testing hardware.
You’re welcome to ask me questions!

## Slide 94: 8. Conclusion
It all must come to an end…

## Slide 95: Conclusion
Raspberry Pi is a PC, but can interface easily with electronics with GPIO pins
You’ve seen a variety of sample projects and parts and how to code with them
Hopefully you’re inspired to hack together your own projects

## Slide 96: Thanks!
Slides: sarahwithee.com/raspberrypi
Share your stories and questions!
Twitter: @geekygirlsarah
Email: hello@sarahwithee.com