## Slide 1: Intro to Hacking with the Raspberry Pi
Sarah Withee
@geekygirlsarah

## Slide 3: Hello!
I am Sarah Withee
Friendly polyglot software engineer
Hardware tinkerer
Robot builder
You can find me at @geekygirlsarah

## Slide 4: A Few Questions To Start…
Who has heard of the Raspberry Pi?
Who owns at least one?
Is it sitting in a closet/junk drawer?
Are you daunted at the idea of tinkering with hardware or electronics?
This talk is probably for you!

## Slide 5: A Few Questions To Start…
If you:
understand circuitry basics,
are familiar with breadboards and wiring,
and know how to program GPIO pins on the Pi
This talk may not be for you.
(I won’t be offended if you leave)

## Slide 6: Breakdown
Raspberry Pi Information and Models
Intro to Hardware
Intro to Programming Hardware
Project 1 - ?
Project 2 - ?
Project 3 - ?
Future Project Inspriation
Conclusion

## Slide 7
“The Raspberry Pi is a credit-card sized computer that plugs into your TV and a keyboard. It is a capable little computer which can be used in electronics projects, and for many of the things that your desktop PC does, like spreadsheets, word-processing and games. It also plays high-definition video. We want to see it being used by kids all over the world to learn programming.”
Raspberry Pi Foundation, raspberrypi.org/faqs

## Slide 8
C
“We are taking back the term ‘Hacking’ which has been soured in the public mind. Hacking is an art form that uses something in a way in which it was not originally intended. This highly creative activity can be highly technical, simply clever, or both. Hackers bask in the glory of building it instead of buying it, repairing it rather than trashing it, and raiding their junk bins for new projects every time they can steal a few moments away.”
Hackaday, hackaday.com/about/

## Slide 9: Resources
Slides, diagrams,
videos, and more!
sarahwithee.com/raspberrypi
very code
much resources
how to pi
total wow

## Slide 10: 1. Raspberry Pi Information and Models
The basics of this delightful computer

## Slide 11: History of the Raspberry Pi
2006 – Had idea for affordable computer for kids
2008 – Processors became cheap enough to make it feasible to build
2011 – 50 alpha boards, 25 beta boards, 10,000 production boards
2012 – Sold first units
2013 – Sold > 2M units
2015 – Pi 2 Model B and Pi Zero released
2016 – Pi 3 Model b released
2017 – Pi Zero W released

## Slide 12: Raspberry Pi Models
Pi Model A+
Pi 3 Model B
Pi Model B+
Pi Zero
Pi 2 Model B
Pi Zero W

## Slide 13: Raspberry Pi Model Comparisons
 |  | Processor | Speed | Memory (shared w/GPU) | Expansion | USB Ports | Ethernet/ Wireless/ Bluetooth | Cost | Power Supply Needed
Pi Model A+ +* |  | ARMv6 (32-bit) | 700 MHz | 512 MB | Micro SDHC | 1 | None | $20 | 700 mA
Pi Model B+ * |  | ARMv6 (32-bit) | 700 MHz | 512 MB | Micro SDHC | 4 | 10/100 mbps | $25 | 1.8 A
Pi 2 Model B |  | ARMv8 (64-bit) | 900 MHz | 1 GB | Micro SDHC | 4 | 10/100 mbps | $35 | 1.8 A
Pi 3 Model B |  | ARMv8 (64-bit) | 1.2 GHz | 1 GB | Micro SDHC/ USB Boot | 4 | 10/100, 802.11n, BT 4.1 | $35 | 2.5 A
Pi Zero |  | ARMv6 (32-bit) | 1.0 GHz | 512 MB | Micro SDHC | 1 | None | $5 | 1.2 A
Pi Zero W |  | ARMv6 (32-bit) | 1.0 GHz | 512 MB | Micro SDHC | 1 | 801.11n, BT 4.1 | $10 | 1.2 A

## Slide 14: 2. Intro to Hardware
Wires and circuits and breadboards, oh my!

## Slide 15: Circuits
A complete route that electricity can travel through
🔌

## Slide 16: Intro to Hardware – Circuits
Series Circuit
Electricty can flow one direction
Close the switch to make the complete path
Open the switch to stop the electric flow

## Slide 17: Intro to Hardware – Circuits
Parallel Circuit
Electricty can flow more than one direction
Close the switch to make both paths complete
Open the switch to stop all the flow

## Slide 18: Breadboards
Device to quickly prototype circuits without solder

## Slide 19: Intro to Hardware - Breadboards
A literal breadboard
(http://www.instructables.com/id/Use-a-real-Bread-Board-for-prototyping-your-circui/)

## Slide 20: Intro to Hardware - Breadboards
Prototype Circuit
(https://learn.sparkfun.com/tutorials/how-to-use-a-breadboard)

## Slide 21: Intro to Hardware - Breadboards
Breadboard features
(https://learn.sparkfun.com/tutorials/how-to-use-a-breadboard)

## Slide 22: Intro to Hardware - Breadboards
Terminal Strips and Power Rails
(https://learn.sparkfun.com/tutorials/how-to-use-a-breadboard)

## Slide 23: Intro to Hardware – Breadboards
Circuits on Breadboards
Provide power to the power rails
Red – positive
Black/blue – negative
Use wires to connect components together

## Slide 24: Intro to Hardware – Breadboards
Circuits with Raspberry Pis
Use pin labelled “+3.3V” (volts) for postive
Use pin labelled “Ground” (GND) for negative

## Slide 25: Intro to Hardware – Breadboards
Circuits with Raspberry Pis
Note: Arduinos use 5V, be careful not to confuse the two

## Slide 26: GPIO
General Purpose Input/Output
Or how our projects “talk” to the Pi

## Slide 27: Intro to Hardware – GPIO
Raspberry Pi Pins
40 hardware pins
2 +3.3V
2 +5V
8 Ground
20 GPIO
2 Miscellaneous
Unfortunately, not labelled ON the Pi

## Slide 28: Intro to Hardware – GPIO
Raspberry Pi Pins
Of course, they’re not in any distinguishable order
(Pin diagram available at talk website)

## Slide 29: 3. Intro to Programming Hardware
The part you’re really here for

## Slide 30: Intro to Programming Hardware
On the Raspberry Pi, Python is built-in with GPIO libraries installed
Other languages available too

## Slide 31: Intro to Programming Hardware – Setup Commands
Pin Mode
First, pick your mode
Board – physical pin #
BCM – GPIO pin #

## Slide 32: Intro to Programming Hardware – Setup Commands
Next, import the GPIO library:
import Rpi.GPIO as GPIO
Then, set the mode (pick one):
GPIO.setmode(GPIO.BOARD)
GPIO.setmode(GPIO.BCM)

## Slide 33: Intro to Programming Hardware – Setup Commands
Pins used should be set to be input or output:
GPIO.setup(3, GPIO.OUT)
GPIO.setup(4, GPIO.IN)
You can change these later, not but setting them at all causes problems

## Slide 34: Intro to Programming Hardware – Output Commands
To write out to the output pins:
(pin number, value)
GPIO.output(3, True)
GPIO.output(10, False)
GPIO.output(6, GPIO.HIGH)
GPIO.output(22, GPIO.LOW)
True and HIGH are “on” (3.3 V)
False and LOW are “off” (0 V)

## Slide 35: Intro to Programming Hardware – Input Commands
To read from the input pins:
(pin number)
x = GPIO.input(4)
sensor.setValue(GPIO.input(15))
Values will be True/False or 1/0
(Note: Arudinos have analog value inputs. Raspberry Pis to not.)

## Slide 36: Intro to Programming Hardware – Cleanup Commands
Finally, when your program ends, you should “clean up” the pins:
GPIO.cleanup()
This stops reading inputs and stops sending outputs.

## Slide 37: Intro to Programming Hardware
Setup recap:
Import Rpi.GPIO library
Set pin mode (GPIO.BOARD or GPIO.BCM)
Set up input/output pins
Runtime recap:
Output a value to a pin number
Save input value from a pin to a variable

## Slide 38: 4. Project 1 - LEDs
The “Hello World” of electronics

## Slide 39: Project 1 - LEDs
8 LEDs that blink back and forth
Battlestar Galactica cylon
Knight Rider KITT car

## Slide 40: Project 1 - LEDs
Materials:
Raspberry Pi and power supply
1 breadboard
8 LEDs
8 resistors
9 jumper wires

## Slide 41: LED
Light-emiting diode
Like a small light bulb

## Slide 42: Project 1 - LEDs
LEDs
Diode – ensures electricity only goes one direction
(Wired wrong, it doesn’t work)
Anode – longer wire (+)
Cathode – shorter wire (-)
ALWAYS use a resistor

## Slide 43: Resistor
Slows down (or resists) the flow of electricity

## Slide 44: Project 1 - LEDs
Resistors
Can wire either direction
Band colors tell resistance value (in Ohms)
Without these, LEDs glow bright white, then element explodes

## Slide 45: Project 1 - LEDs
Wiring
Wire Pi’s ground to ground rail (black wire)
Plug in LEDs across gap

## Slide 46: Project 1 - LEDs
Wiring
Connect resistors from LED cathodes (-) to ground
Connect anodes (+) to Pi GPIO pins
GPIO pins become power sources

## Slide 47: Project 1 - LEDs
Programmatically turn on power to blue wires
Through LED & Resistor
Return to Ground
Through blue GND rail

## Slide 48: Project 1 - LEDs
# Import libraries
import RPi.GPIO as GPIO
import time
# Create array of GPIO pins
pins = [3, 5, 7, 29, 31, 26, 24, 21]
# Speed lights will blink (secs)
speed = .2 # Cylon-approved speed

## Slide 49: Project 1 - LEDs
# Set GPIO pins to board (physical pins) mode
GPIO.setmode(GPIO.BOARD)
# Set up all pins as output pins
for pin in pins:
GPIO.setup(pin, GPIO.OUT)

## Slide 50: Project 1 - LEDs
while True:
for i in range(len(pins)):
GPIO.output(pins[i], True)
time.sleep(speed)
GPIO.output(pins[i], False)
for i in range(len(pins)-1, -1, -1):
GPIO.output(pins[i], True)
time.sleep(speed)
GPIO.output(pins[i], False)

## Slide 51: Project 1 - LEDs
while True:
for i in range(len(pins)-1):
GPIO.output(pins[i], True)
time.sleep(speed)
GPIO.output(pins[i], False)
for i in range(len(pins)-1, 0, -1):
GPIO.output(pins[i], True)
time.sleep(speed)
GPIO.output(pins[i], False)

## Slide 52: Project 1 - LEDs

## Slide 53: 5. Project 2 – Sensors
Teaching computers to see.
Or something.

## Slide 54: Ultrasonic Distance Sensor
Looks like robot, but measures distance with timed sound waves

## Slide 55: Project 1 - LEDs
Ultrasonic Distance Sensor
Sends ultrasonic (high-pitched 40KHz) sound wave
Detects time it takes for sound to bounce back
Time tells it the distance

## Slide 56: Project 1 - LEDs
Ultrasonic Distance Sensor
4 pins:
VCC (power)
Trig (trigger)
Echo
GND (ground)
One side transmits, one receives

## Slide 57: Project 1 - LEDs
Materials:
Raspberry Pi and power supply
1 breadboard
8 LEDs
8 resistors
9 jumper wires

## Slide 58: 6. Project 3 – Push Buttons and LCD screens
Push it, push it real good